## Slide 1: Grids of Thrones

## Slide 2
Today:
  grdraster
  grdgradient
  Grdimage
  Cpt files
This is plenty for hours and hours… but we will get just the flavor of it so you can use and reuse these commands

## Slide 3
Grdraster [filenumber | “text patern”] –Rwest/east/south/north[r] … there are more options (we will use the minimum here)
Search for the file in dbase/grdraster.info
In case your GMT does not have these files… we will work with either:
http://www.ngdc.noaa.gov/mgg/global/relief/ETOPO1/data/bedrock/grid_registered/netcdf/
Or the file that will be in the folder…

## Slide 4
We can make grids without having to make big scripts, but if it is a figure that needs to be repeated several times you can just leave the gridding inside your script.
The line:
‘grdraster 9 -R-16/-4/33/45 -Gmainland.nc -V’
  extracts a region from a binary raster file (specified byt the -R and writes a grid file)
  Writes to a file specified in the –G
  ‘-V’ is verbose (tells me some details)
  Where does the “a come from”?

## Slide 5
That ‘1’ matches a number in a file called grdraster.info (there is one in the folder, open it)…
file_number "title string" "z units" -R -I GorP type scale offset NaNflag filename [L|B] [H<bytes>]
9
"ETOPO2 global topography" "m" -R-180/180/-90/90 -I2m P i 1 0 none ETOPO2.raw.bin B
File_number = 1
“title string” = "ETOPO2 global topography”
“z units” = "m”
-R = -R-180/180/-90/90 some cases can be 0/360/-90/90, or other restrictions
-I = -I2m -> x_inc[/y_inc] describes the sampling interval
GorP = P -> is either G or P, indicating Grid or Pixel registration.
Type = i -> indicating the kind of data stored in the raster, in this case:
i: signed two-byte integer data
Scale = 1 -> number which should be multiplied on the raster value after read
Offset = 0 -> number which should be added to the [scaled] raster value
NaNflag = none -> number which is written in the raster to represent NaN.
If all values in the raster represent data, NaNflag is none.
Filename = ETOPO2.raw.bin -> name the raster file
[L|B] = B -> BYTE-ORDER (Big-endian) this is OPTIONAL
[H<bytes>] = # of bites. This is used in case your raster file has a header, grdraster will skip the first # of bites of the file.
ALL THIS INFORMATION IS IN THE grdraster.info‘’ anyway

## Slide 6
So, here is where, if we can use the file and we are successful, we can produce out own .grd file.
If not, we can use a .nc file that should be in the working folder of today’s class: mainland.nc
Lets see that grid, if a grid file is made correctly, we don’t have to guess what it has, and its limits, we can just ask this way:
  grdinfo mainland.nc

## Slide 7
Next up, grdimage, and cpt fileswhich is better seen in the examples…..